## Mic Schematic

Drake TR-7, Kenwood TR-7400

The Transmit Signal is shown from connector pin 1 to the mic symbol.
PTT is shown from connector pin 2 through a switch to ground.
Ground is shown from connector pins 3 and 4 to the ground symbol.

## Speaker Plug

Mono plug (to speaker jack)
Tip of plug - Receive Signal
Sleeve of plug - Ground